## Slide 1
Types of Solids
Solids
liquids
Gases
Plasmon* (not within the course)
* A plasma is a hot ionized gas consisting of approximately equal numbers of positively charged ions and negatively charged electrons. The characteristics of plasmas are significantly different from those of ordinary neutral gases

## Slide 2
Solids used in our daily life

## Slide 3
Types of Metals

## Slide 5
Solids
Crystalline
Non-crystalline (Amorphous)
Any solid having orderly three dimensional arrangement of atoms is called crystalline solid or crystal.
e.g. Salt (NaCl), Iron, Aluminium, Gold, Silver
Any solid consists of random arrangements of atoms is called amorphous solid.
e.g. glass, polymers

## Slide 12
Crystal Structure = Space Lattice + Basis
Basis attached to each lattice point called crystal structure
The number of atoms in the basis may be one or more than one

## Slide 13
Space lattice:
A regular geometrical arrangement of points in space is called space lattice
Lattice constant or lattice parameter:
The distance between two identical lattice points in one direction is called lattice constant or lattice parameter.
One dimensional lattice
Two dimensional lattice
Three dimensional lattice

## Slide 17
Unit cell:
The smallest geometrical entity whose repetition gives the crystal is called unit cell

## Slide 20
BCC

## Slide 21
FCC

## Slide 23
A minimum volume unit cell and has only one lattice point it is called primitive cell.
e.g simple cubic (SC)
Primitive cell
A minimum volume unit cell and has more than one lattice point it is called non-primitive cell. The primitive cell represented by a symbol is “P”
e.g. Body centered cubic (BCC), Face centered cubic (FCC), Base centered or end centered.
Non-Primitive cell

## Slide 24
Unit cell | Type | Symbol
Simple cubic | Primitive | P
Body centered cubic | Non-primitive | I
Face centered cubic | Non-primitive | F
End centered or base centered | Non-primitive | C
Primitive
Base centered or end centered
Body centered cubic (BCC)
Face centered cubic (FCC)

## Slide 25
Crystal Systems
System | Axis length and Angles | Examples
Cubic | a = b = c, α = β = γ = 90° | Au, Ag, Fe
Tetragonal | a = b ≠ c, α = β = γ = 90° | In, Pa
Orthorhombic | a ≠ b ≠ c, α = β = γ = 90° | Bi, Sb, As
Rhombohedral (or Trigonal) | a = b = c, α = β = γ ≠ 90° | SiO2, CaCO3
Hexagonal | a = b ≠ c, α = β = 90° and γ = 120° | Se, Te
Monoclinic | a = b ≠ c, α = γ = 90° ≠ β | Na2SO4, CaSO4
Triclinic | a ≠ b ≠ c, α ≠ β ≠ γ ≠ 90° | CuSO4, K2Cr2O7

## Slide 27
The Bravais lattice are the distinct lattice types which when repeated can fill the whole space.
14 Bravais Lattices

## Slide 28
System | Axis length and Angles | Bravais Lattice | Symbol
Cubic | a = b = c, α = β = γ = 90° | Simple Body centered Face centered | P I F
Tetragonal | a = b ≠ c, α = β = γ = 90° | Simple Body centered | P B
Orthorhombic | a ≠ b ≠ c, α = β = γ = 90° | Simple Body centered Face centered End centered | P I F C
Rhombohedral (or Trigonal) | a = b = c, α = β = γ ≠ 90° | Simple | P
Hexagonal | a = b ≠ c, α = β = 90° and γ = 120° | Simple | P
Monoclinic | a = b ≠ c, α = γ = 90° ≠ β | Simple End centered | P C
Triclnic | a ≠ b ≠ c, α ≠ β ≠ γ ≠ 90° | Simple | P
Bravais Lattice

## Slide 29
The number of equidistant nearest neighbour atoms in crystal.
Coordination number
SC = 1
BCC = 2
FCC = 4
Number of atoms or lattice points in unit cell
SC = 1
BCC = 8
FCC = 12

## Slide 30
The distance between two centers of neighbouring atoms is called nearest neighbour distance
Nearest neighbor distance
For Simple cubic,
For Body centered cubic,
For Face centered cubic,

## Slide 31
Primitive unit cell or simple cubic
a
r
a
r

## Slide 32
Body centered cubic

## Slide 33
a
a
Face centered cubic
4r = a

## Slide 34
Atomic packing factor
where
where
where

## Slide 35
 | Simple Cubic | Body centered cubic | Face centered cubic
No. of atoms or lattice points per unit cell | 1 | 2 | 4
No. of nearest neighbors (Coordination number) | 6 | 8 | 12
Nearest neighbor distance | a |  | 
Packing fraction |  |  | 74
 | Simple Cubic | Body centered cubic | Face centered cubic
No. of atoms or lattice points per unit cell | 1 | 2 | 4
No. of nearest neighbors (Coordination number) | 6 | 8 | 12
Nearest neighbor distance | a |  | 
Packing fraction |  |  |